## Slide 1: IK2227 – Lab 4: RDMA
Slides by: M. Scazzariello

## Slide 2: recap on Infiniband
Infiniband (IB) is a network stack designed for HPC
TCP is packet-oriented, IB is message-oriented
  the low-level details are offloaded/managed by the NIC
offloads the whole network stack into the NIC
  high performance (low latency, high throughput)
  kernel is involved only in the initialization of connections
apps use Infiniband Verbs to interact with the NIC

## Slide 3: Infiniband verbs
two main types
  two-sided verbs: both sender and receiver are active parts in the communication
    SEND: sender posts a request to send some data
    RECV: receiver posts a request preparing buffers to store data; NIC generates a completion event once the transmission is complete
    CPU is involved in posting RECV and handling the completion events
  one-sided verbs: only the sender is the active part in the communication, the receiver is passive
    RDMA verbs
    no CPU intervention, high performant

## Slide 4: Remote Direct Memory Access (RDMA)
RDMA is a key feature of Infiniband
  enables direct memory access between nodes
requires a RDMA-capable NIC (in short RNIC)
data directly moves from the RNIC to the main memory
  and viceversa
  bypasses CPU, caches, and OS
sender/remote host app is unaware of the operation
  needs additional mechanisms for notifications in userspace

## Slide 5: RDMA verbs
RDMA Write: the sender writes data into a registered memory region of the remote host
  data to send must be in sender’s local memory
    both main memory or GPU memory (with GPUDirect)
RDMA Read: the sender reads data from a registered memory region of the remote host
  sender must specify a local memory area where to receive data
    both main memory or GPU memory (with GPUDirect)
Fetch & Add: increments the value at a specified address by a specified amount (in the remote host's memory)
Compare & Swap: compare the value at a specified address with a specified value and if they are equal, a specified value will be stored at the address (in the remote host's memory)

## Slide 6: RDMA verbs
RDMA Write: the sender writes data into a registered memory region of the remote host
  data to send must be in sender’s local memory
    both main memory or GPU memory (with GPUDirect)
RDMA Read: the sender reads data from a registered memory region of the remote host
  sender must specify a local memory area where to receive data
    both main memory or GPU memory (with GPUDirect)
Fetch & Add: increments the value at a specified address by a specified amount (in the remote host's memory)
Compare & Swap: compare the value at a specified address with a specified value and if they are equal, a specified value will be stored at the address (in the remote host's memory)

## Slide 7: RDMA over Converged Ethernet (RoCE)
Infiniband is incompatible with Ethernet networks
RDMA over Converged Ethernet (RoCE)
  basically, IB transport that runs over standard Ethernet
  enables IB verbs without an Infiniband network
RoCEv1 encapsulates IB transport in Ethernet frames
  legacy, not used anymore
RoCEv2 encapsulates IB transport in IP/UDP
  Layer-4 routable (with ECMP, see Lab 1)
  requires RNIC support (almost every RNIC has it)
  widely used in today’s datacenters

## Slide 8: Infiniband terminology (1)
Queue Pair (QP)
  pair of queues, i.e., Send Queue (SQ) & Receive Queue (RQ)
  used for communication between two endpoints
Work Request (WR)
  high-level operation (i.e., unified API) that is submitted to a WQ
  specifies the operation and the memory region involved
  each WR results in a Work Queue Entry (WQE)
Work Queue (WQ)
  structure holding Work Queue Entries (WQEs) for pending operations
Work Queue Entry (WQE)
  low-level (i.e., RNIC driver) command posted to a Work Queue

## Slide 9: Infiniband terminology (2)
Completion Queue (CQ)
  queue that tracks completed WQ operations
  multiple QPs can share a single CQ
Completion Queue Entry (CQE)
  entry in the CQ
  indicates the completion status of a WQE
  allows applications to check for successful/failed operations

## Slide 10: sender example
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
post
WR
poll (DMA)
WQE
Completion Queue
WQE

## Slide 11: sender example
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
Completion Queue
process request and send on the wire
WQE
WQE

## Slide 12: sender example
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
Completion Queue
operation successful!
WQE

## Slide 13: sender example
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
Completion Queue
operation successful!
CQE
generate CQE

## Slide 14: receiver example (for two-sided)
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
Completion Queue
RECV
memory
data
operation successful!

## Slide 15: receiver example (for two-sided)
Queue Pair
Receive Queue
Send Queue
application
host memory
Work Queue
RNIC
Completion Queue
operation successful!
memory
data
CQE
generate CQE

## Slide 16: implementation

## Slide 17: Infiniband Verbs in Linux
ibverbs is the C userspace library in Linux
  provides access to Infiniband/RoCE and RNICs
APIs to manage connections and resources from user applications
pyverbs is the Python wrapper of ibverbs
  exposes the same set of APIs in a simplified manner
  ibverbs is preferred for high performance
  we will use pyverbs for simplicity! 

## Slide 18: Infiniband connection
the two peers need to establish an IB connection
  different from a standard TCP/UDP socket
  managed by the host CPU
requires an additional off-band mechanism (usually, TCP) to exchange connection information
once the connection is successfully initialized, Work Requests can be posted on Queue Pairs

## Slide 19: Infiniband connection lifecycle
off-band TCP connection with the remote peer
memory registration
  allocate and register memory to be accessible by the RNIC
  generate memory keys (local key/remote key) for access control
Queue Pair (QP) creation and configuration
  create a QP and configure it to move in the RTS (Ready-to-Send) state
  exchange QP information (QP number, remote key) with the remote peer
CQ polling thread creation
request posting
  post operations (WR) to the WQ
completion handling
  trigger application logic based on CQEs

## Slide 20: pre-flight check
verify that the requested device exists
devices_list = pyverbs.device.rdma_get_devices()
found = False
for device in devices_list:
device_name_str = device.name.decode('utf-8')
if device_name_str == "rxe0":
found = True
break
if not found:
print(f"Interface {iface} not found.", file=sys.stderr)
sys.exit(1)
get all RDMA devices
iface name

## Slide 21: off-band TCP connection
sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
try:
sock.connect(("10.0.0.3", 18515))
except Exception as ex:
print("Error connecting to server:", ex, file=sys.stderr)
sys.exit(1)
TCP socket
server address and port (chosen by us)
client: TCP connection with the remote peer
server_sock = socket.socket(socket.AF_INET, socket.SOCK_STREAM)
server_sock.bind(('', 18515))
server_sock.listen(1)
conn, addr = server_sock.accept()
server: listens to TCP connections from remote peers
bind 0.0.0.0:18515 (chosen by us)
listen to max 1 connection
accept connection from the client

## Slide 22: memory registration
open a context with the RDMA device
  used to allocate resources for the device (QP, memory, etc.)
register a Protection Domain (PD) in the context
  group of resources (QP, memory, etc.) that share access permissions
  isolation between different RDMA resources (of different processes)
with pyverbs.device.Context(name="rxe0") as ctx:
with pyverbs.pd.PD(ctx) as pd:
mr = pyverbs.mr.MR(
pd,
4096,
IBV_ACCESS_LOCAL_WRITE | IBV_ACCESS_REMOTE_WRITE
)
PD associated with the memory region
size in bytes
access flags for this MR, local processes can write it, remote peers can write

## Slide 23: QP creation
each QP needs a Completion Queue associated
  we first create the CQ
create the QP by configuring its capacity
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
cq = pyverbs.cq.CQ(ctx, 10, None, None, 0)
qp_init_attr = pyverbs.qp.QPInitAttr(
qp_type=IBV_QPT_RC,
scq=cq,
rcq=cq,
cap=pyverbs.qp.QPCap(
max_send_wr=8192,
max_recv_wr=8192,
max_send_sge=32,
max_recv_sge=32
)
)
qp = pyverbs.qp.QP(pd, qp_init_attr)
CQ capacity, it can contain 10 CQEs (that need to be consumed!)
type of QP, RC=Reliable Connection supports all the verbs
CQ associated with the QP (both for Send and Receive queues)
max WRs that can be posted on Send and Receive queues, respectively
max SGEs (explained later) that can be posted on Send and Receive queues, respectively

## Slide 24: QP configuration
the QP is created into the RESET state
we need to configure to bring its state into RTS
first transition is RESET->INIT
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
init_attr = pyverbs.qp.QPAttr(
qp_state=IBV_QPS_INIT,
port_num=1
)
init_attr.pkey_index = 0
init_attr.qp_access_flags = IBV_ACCESS_REMOTE_WRITE
qp.modify(init_attr, IBV_QP_STATE | IBV_QP_PKEY_INDEX | IBV_QP_PORT | IBV_QP_ACCESS_FLAGS)
state to transition into
if a device has multiple ports, which one to use, in this case we have only 1
partition keys table for this QP, leave 0
chooses which remote operations are allowed on the QP, default (0) is only local
fields we are modifying on the QP (the ones required by the INIT transition)

## Slide 25: QP configuration
next transition is INIT->RTR (Ready-To-Receive)
  client needs to receive remote peer QP information to transition
  remote peer needs our QP information to transition
we will send
  QP number: identifier of the QP, automatically assigned
  rkey: auth key that remote peer uses to access our memory
  MR address: the starting address of our buffer
  local interface GID: in RoCEv2 is the local interface IP

## Slide 26: QP configuration
receive remote peer QP information
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
remote_data = recvn(sock, ctypes.sizeof(QpConnectionData))
if len(remote_data) != ctypes.sizeof(QpConnectionData):
print("Error receiving connection info from server", file=sys.stderr)
sys.exit(1)
remote_con = QpConnectionData.from_buffer_copy(remote_data)
# at the beginning of the Python script
class QpConnectionData(ctypes.BigEndianStructure):
_pack_ = 1
_fields_ = [
('qp_num', ctypes.c_uint32),
('rkey', ctypes.c_uint32),
('addr', ctypes.c_uint64),
('gid', ctypes.c_ubyte * 16)
]
Python serializable data structure
receive from remote and check integrity
deserialize bytes into the data structure

## Slide 27: QP configuration
send local QP information to remote peer
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
local_gid = ctx.query_gid(port_num=1, index=1)
byte_gid = ipaddress.ip_address(local_gid.gid).packed
local_con_obj = QpConnectionData()
local_con_obj.qp_num = qp.qp_num
local_con_obj.rkey = mr.rkey
local_con_obj.addr = mr.buf
local_con_obj.gid[:] = byte_gid
sock.sendall(bytes(local_con_obj))
get the GID from port=1, index is the GID we want to get, in the lab 0 is the IB GID, 1 is the RoCEv2 GID
local_gid.gid is a string, convert to bytes for serialization using ipaddress
create and populate the data structure
serialize it (calling bytes) and send to remote

## Slide 28: QP configuration
prepare and perform INIT->RTR transition
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
rtr_attr = pyverbs.qp.QPAttr(
qp_state=IBV_QPS_RTR,
path_mtu=IBV_MTU_1024
)
rtr_attr.dest_qp_num = remote_con.qp_num
rtr_attr.rq_psn = 0
rtr_attr.max_dest_rd_atomic = 1
rtr_attr.min_rnr_timer = 31
the maximum payload size between the two QPs, different from the physical MTU
the remote QP to connect to, received from the socket
remote starting PSN
state to transition into
max RDMA reads (or atomic operations) that this QP can handle as a receiver
max NAK timer, the value 31 corresponds to 491.52s (mapping is available in docs)

## Slide 29: QP configuration
prepare and perform INIT->RTR transition
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
remote_gid_str = ipaddress.ip_address(bytes(remote_con.gid)).exploded
gr = pyverbs.addr.GlobalRoute(
dgid=pyverbs.addr.GID(val=remote_gid_str),
sgid_index=1
)
ah_attr = pyverbs.addr.AHAttr(
gr=gr,
is_global=1,
port_num=1
)
rtr_attr.ah_attr = ah_attr
qp.modify(rtr_attr, IBV_QP_STATE | IBV_QP_PATH_MTU | IBV_QP_DEST_QPN | IBV_QP_RQ_PSN | IBV_QP_MAX_DEST_RD_ATOMIC | IBV_QP_MIN_RNR_TIMER | IBV_QP_AV)
remote_con.gid are bytes, convert to string using ipaddress
GID of the remote peer, received from the socket
path information to reach remote, is_global=1 - using a GID
port_num=1 - port to reach the remote GID
source GID index, 1 since we are using RoCEv2

## Slide 30: QP configuration
we are in RTR, the RTR->RTS transition can be performed locally
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
rts_attr = pyverbs.qp.QPAttr(
qp_state=IBV_QPS_RTS
)
rts_attr.sq_psn = 0
rts_attr.timeout = 14
rts_attr.retry_cnt = 7
rts_attr.rnr_retry = 7
rts_attr.max_rd_atomic = 1
qp.modify(
rts_attr,
IBV_QP_STATE | IBV_QP_TIMEOUT | IBV_QP_RETRY_CNT | IBV_QP_RNR_RETRY | IBV_QP_SQ_PSN | IBV_QP_MAX_QP_RD_ATOMIC
)
local starting PSN
min timeout a QP waits for ACK/NAK before retransmission, 14 equals to 67.1ms
# of times the QP tries resend a pkt before reporting an error, 7 = infinite
state to transition into
# of times the QP tries to resend a pkt when receiving a NAK, 7 = infinite
max RDMA reads (or atomic operations) that this QP can handle as a sender

## Slide 31: CQ polling thread creation
we are in RTS state, the two QPs can communicate!
we spawn a thread that polls the CQ for CQEs
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
global keep_polling
keep_polling = True
cq_thread = threading.Thread(target=poll_cq, args=(cq,))
cq_thread.start()
# at the beginning of the Python script
keep_polling = True
def poll_cq(cq: pyverbs.cq.CQ) -> None:
global keep_polling
while keep_polling:
wc_num, wc_list = cq.poll(num_entries=10)
if wc_num > 0:
for wc in wc_list:
print(f"CQE: wr_id={wc.wr_id}, status={wc.status}")
global flag to stop the thread when the app ends
poll the CQ, blocking call, return 10 entries (the capacity of our CQ)
print CQE data, but apps can use these signals to trigger app logic
create a thread that runs the poll_cq function with cq as argument and start it

## Slide 32: posting verbs (two-sided)
client side
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
message = b"Hello from IK2227!"
mr.write(data=message, length=len(message) + 1, offset=0)
sge = pyverbs.wr.SGE(
addr=mr.buf,
length=len(message) + 1,
lkey=mr.lkey
)
wr = pyverbs.wr.SendWR(
wr_id=1,
sg=[sge],
num_sge=1,
opcode=IBV_WR_SEND
)
qp.post_send(wr)
starting local address for data read
length of the data to read
auth key for accessing the local MR
write some data in the buffer
user-defined ID to identify the WR
SGE list composing the WR
type of operation
post on the SQ

## Slide 33: posting verbs (two-sided)
server side
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
sge = pyverbs.wr.SGE(
addr=mr.buf,
length=4096,
lkey=mr.lkey
)
recv_wr = pyverbs.wr.RecvWR(
wr_id=1,
sg=[sge],
num_sge=1
)
qp.post_recv(recv_wr)
starting local address to receive data
length of the data to receive
auth key for accessing the local MR
post on the RQ

## Slide 34: posting verbs (one-sided)
client side only, server is unaware of the operation
with pyverbs.device.Context(name="rxe0") as ctx:
# ... previous code
message = b"Hello from IK2227!"
mr.write(data=message, length=len(message) + 1, offset=0)
sge = pyverbs.wr.SGE(
addr=mr.buf,
length=len(message) + 1,
lkey=mr.lkey
)
wr = pyverbs.wr.SendWR(
wr_id=1,
sg=[sge],
num_sge=1,
opcode=IBV_WR_RDMA_WRITE
)
wr.set_wr_rdma(rkey=remote_con.rkey, addr=remote_con.addr)
qp.post_send(wr)
remote auth key to access remote memory (received through the socket)
starting remote address to write data (received through the socket)

## Slide 35: Scatter-Gather Entry (SGE)
data structure used to describe memory buffers for transfers
WQEs can contain one or more SGEs, specifying the memory regions involved in the operation
WR
wr_id
num_sge=2
sg
SGEs
addr=0xbcde
length=N1 B
lkey
addr=0xcdef
length=N2 B
lkey
N1 Bytes
N2 Bytes
Memory
0
1
mr.buf = 0xabcd
0xbcde
accesses 0xbcde;
authorized by lkey
0xcdef
accesses 0xcdef;
authorized by lkey

## Slide 36: lab deep dive

## Slide 37: lab pre-conditions
download the VM for your architecture from Canvas!
  the VM can be found in the “Labs” page

## Slide 38: lab topology
server
A
client
10.0.0.0/24
eth0
2
eth0
3
rxe0
rxe1
SoftRoCE virtual iface
tapper
eth0

## Slide 39: SoftRoCE
RDMA operations require hardware support
SoftRoCE is a software implementation of RoCE in Linux
  in particular RoCEv2
allows RDMA applications to run without real RNICs
SoftRoCE has poor performance w.r.t. hardware
  all operations are processed by the CPU
useful for emulation
  it mimics RNICs behavior and accesses the same ibverbs APIs

## Slide 40: SoftRoCE configuration example
ip addr add 10.0.0.2/24 dev eth0
rdma link add rxe0 type rxe netdev eth0
client.startup
name of the SoftRoCE iface
physical interface that is used to send RoCE packets
type of the SoftRoCE iface, rxe is RoCE

## Slide 41: goal of the lab
establish an IB connection between client and server
client loads a database of book titles in its local memory that needs to be exchanged with the server

## Slide 42: task 1: complete the lab
configure the server device
write the server.startup file
  configure the correct IP address on eth0
  create the SoftRoCE interface named rxe1, attached to eth0

## Slide 43: start the lab
open a terminal
enter the lab directory (cd lab_directory)
run sudo kathara lstart --privileged
start devices with full root privileges (required by SoftRoCE)
Kathará requires sudo to run in privileged mode

## Slide 44: task 2: complete the IB connections
in the shared folder of the lab you will find two Python scripts
  client.py and server.py
the client-side connection is configured, you need to complete the server-side connection

## Slide 45: task 2: complete the IB connections
open the server.py
as previously discussed, client and server need to exchange QP information to proceed in RTR
the client waits for the server information first
you need to (follow “TODO 1”):
  send server’s local information to the client
    using the socket object called conn
  receive client’s information and decode the result
    using the socket object called conn
hint: you can look at the code of the client side 

## Slide 46: task 3: test the IB connection
test if the IB connection gets established properly
on the server device:
python3 /shared/server.py rxe1
on the client device:
python3 /shared/client.py rxe0 10.0.0.3
you should see “Connection established” on both sides
you can stop the processes by pressing CTRL+C

## Slide 47: task 4: posting two-sided verbs
now we can send the book list from client to server
the book list is already loaded in the client’s local MR
the list is loaded with the following memory layout
title 1 |  |  |  |  |  |  |  |  | 00
ff | ff | ff | ff | ff | ff | ff | ff | ff | ff
title 2 |  |  |  |  |  |  |  |  | 00
ff | ff | ff | ff | ff | ff | ff | ff | ff | ff
... |  |  |  |  |  |  |  |  | 
title 32 |  |  |  |  |  |  |  |  | 00
ff | ff | ff | ff | ff | ff | ff | ff | ff | ff
string terminator
10 Bytes 0xff padding

## Slide 48: task 4: posting two-sided verbs
send the book list using two-sided verbs
on the client device (follow the TODOs):
  prepare a SGE list to read ONLY book titles (without padding)
    the code exposes a dict books in which the key is the book title, and the value is the length of the string
    the code already initializes a sge_buff to move in the buffer (starting MR address)
    the code exposes a PADDING constant that is the length of the padding in bytes
  post a WR (containing the previously defined SGE list) using the SEND verb on the Send Queue
    assign a WR ID = 1 to the request

## Slide 49: task 4: posting two-sided verbs
send the book list using two-sided verbs
on the server device (follow “TODO 2”):
  prepare a single SGE to receive data
    SGE writes data starting from the first MR location (mr.buf)
    the length is BUFFER_SIZE (we do not know the size of the data)
  post a WR (containing the previously defined SGE) on the Receive Queue
    assign a WR ID = 1 to the request

## Slide 50: task 4: test the data exchange
let’s test if the data is exchanged correctly
first, let’s start a tcpdump on the tapper device:
tcpdump -i eth0 -w /shared/send.pcap
on the server device:
python3 /shared/server.py rxe1
on the client device:
python3 /shared/client.py rxe0 10.0.0.3
stop all the scripts (and tapper) using CTRL+C

## Slide 51: task 4: test the data exchange
what is the result of the operation on client and server?
is the list of book titles printed on the server?
can you explain all the steps of the operation?
from the shared folder in the lab directory, open the send.pcap file using Wireshark
  can you identify the off-band TCP communication?
  how many RoCEv2 packets are exchanged?
  what is the UDP destination port of RoCEv2?
  what is the payload of the packet? 

## Slide 52: task 5: posting one-sided verb
send the book list using one-sided verb
  we want the client to write in the remote memory (RDMA Write)
server.py needs to be modified to handle remote operations
copy the server.py script into a new file server_rdma.py
in server_rdma.py
  change the MR initialization flags to accept remote writes
    add the IBV_ACCESS_REMOTE_WRITE flag
  change the QP access flags (in the INIT transition) to make the QP able to handle remote operations
    add the IBV_ACCESS_REMOTE_WRITE flag
  remove the posting of the WR on the Receive Queue

## Slide 53: task 5: posting one-sided verb
send the book list using one-sided verb
client.py needs to be modified to post a RDMA Write
copy the client.py script into a new file client_rdma.py
in client_rdma.py
  change the type of WR to post (with the same SGE list)
    change the operation to IBV_WR_RDMA_WRITE
  configure the RDMA WR fields
    through the wr.set_wr_rdma method
    we want to write from the starting address of the remote MR

## Slide 54: task 5: test the data exchange
let’s test if the data is exchanged correctly
first, let’s start a tcpdump on the tapper device:
tcpdump -i eth0 -w /shared/write.pcap
on the server device:
python3 /shared/server_rdma.py rxe1
on the client device:
python3 /shared/client_rdma.py rxe0 10.0.0.3

## Slide 55: task 5: test the data exchange
what is the result of the operation on client and server?
is the list of book titles printed on the server?
  can you explain why?
from the shared folder in the lab directory, open the send.pcap file using Wireshark
  can you identify the RDMA Write?
  what is the payload?
  extra: look at the IB headers, you can identify all the remote information that we passed when posting the request!

## Slide 56: task 6: RDMA op notification
we need an additional mechanism to notify the RDMA op
two ways:
  poll the MR and check when the first byte != 0
    inefficient!
    used in this lab
  use RDMA Operation With Immediate
    efficient

## Slide 57: task 6: RDMA op notification
poll the MR and check when the first byte != 0
modify server_rdma.py
  after the CQ thread starts, add the following snippet
start again the Python scripts
what is the output on the server?
is the book list now printed on the server?
while mr.read(length=1, offset=0) == b"\x00":
print("Polling memory")
time.sleep(1)
dump_mr(mr)

## Slide 58: stop the lab
open a terminal
enter the lab directory (cd lab_directory)
run kathara lclean